## Slide 1: Race 1 Algorithm
Nick LaRosa and Nolan Sornson

## Slide 2: Extend Disparities
Find disparities by determining where consecutive LIDAR readings differ by greater than a threshold
Set all LIDAR indices within 土θ of all disparities to zero, where θ is given by: and k is some positive safety factor constant
This accounts for the non-zero width of the car

## Slide 3: Find Single Best Point
a
b
* For this to work, car needs to not immediately turn to the new best point *
Single Best Point
Average of Best Points

## Slide 4: Use Best Point Angle as PID Error Input
a
a’
a
a
a’
New Steering Angle to Publish

## Slide 5: Speed Tuning
Modified P-control algorithm, where the speed of the car is given by a piecewise function corresponding to the straight-ahead distance
  Maximum speed if distance is greater than some threshold, otherwise, derate the speed linearly based on the distance
After rounding a corner, do not pop back to maximum speed immediately, but increase the speed linearly over a short time
  Improves stability and prevents loss of control when exiting corners